## Slide 1: Module 3: VLANs
Switching, Routing, and Wireless Essentials v7.0 (SRWE)
Notes: Cisco Networking Academy Program
Switching, Routing, and Wireless Essentials v7.0 (SRWE)
Module 3: VLANs

## Slide 2: 3.1 Overview of VLANs
Notes: 3 – VLANs
3.1 – Overview of VLANs

## Slide 3: Overview of VLANs VLAN Definitions
VLANs are logical connections with other similar devices.
Placing devices into various VLANs have the following characteristics:
  Provides segmentation of the various groups of devices on the same switches
  Provide organization that is more manageable
      Broadcasts, multicasts and unicasts are isolated in the individual VLAN
      Each VLAN will have its own unique range of IP addressing
      Smaller broadcast domains
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.1 – VLAN Definitions

## Slide 4: Overview of VLANs Benefits of a VLAN Design
Benefits of using VLANs are as follows:
Benefits | Description
Smaller Broadcast Domains | Dividing the LAN reduces the number of broadcast domains
Improved Security | Only users in the same VLAN can communicate together
Improved IT Efficiency | VLANs can group devices with similar requirements, e.g. faculty vs. students
Reduced Cost | One switch can support multiple groups or VLANs
Better Performance | Small broadcast domains reduce traffic, improving bandwidth
Simpler Management | Similar groups will need similar applications and other network resources
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.2 – Benefits of a VLAN Design

## Slide 5: Overview of VLANs Types of VLANs
Default VLAN
VLAN 1 is the following:
  The default VLAN
  The default Native VLAN
  The default Management VLAN
  Cannot be deleted or renamed
  Note: While we cannot delete VLAN1 Cisco will recommend that we assign these default features to other VLANs
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs

## Slide 6: Overview of VLANs Types of VLANs (Cont.)
Data VLAN
Dedicated to user-generated traffic (email and web traffic).
VLAN 1 is the default data VLAN because all interfaces are assigned to this VLAN.
Native VLAN
This is used for trunk links only.
All frames are tagged on an 802.1Q trunk link except for those on the native VLAN.
Management VLAN
This is used for SSH/Telnet VTY traffic and should not be carried with end user traffic.
Typically, the VLAN that is the SVI for the Layer 2 switch.
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs (Cont.)

## Slide 7: Overview of VLANs Types of VLANs (Cont.)
Voice VLAN
  A separate VLAN is required because Voice traffic requires:
      Assured bandwidth
      High QoS priority
      Ability to avoid congestion
      Delay less that 150 ms from source to destination
  The entire network must be designed to support voice.
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs (Cont.)

## Slide 8: 3.2 VLANs in a Multi-Switched Environment
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment

## Slide 9: VLANs in a Multi-Switched Environment Defining VLAN Trunks
A trunk is a point-to-point link between two network devices.
Cisco trunk functions:
Allow more than one VLAN
Extend the VLAN across the entire network
By default, supports all VLANs
Supports 802.1Q trunking
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.1 – Defining VLAN Trunks

## Slide 10: VLANs in a Multi-Switched Environment Networks without VLANs
Without VLANs, all devices connected to the switches will receive all unicast, multicast, and broadcast traffic.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.2 – Networks without VLANs

## Slide 11: VLANs in a Multi-Switched Environment Networks with VLANs
With VLANs, unicast, multicast, and broadcast traffic is confined to a VLAN. Without a Layer 3 device to connect the VLANs, devices in different VLANs cannot communicate.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.3 – Networks with VLANs

## Slide 12: 3.3 VLAN Configuration
Notes: 3 – VLANs
3.3 – VLAN Configuration

## Slide 13: VLAN Configuration VLAN Ranges on Catalyst Switches
  Catalyst switches 2960 and 3650 support over 4000 VLANs.
Normal Range VLAN 1 – 1005 | Extended Range VLAN 1006 - 4095
Used in Small to Medium sized businesses | Used by Service Providers
1002 – 1005 are reserved for legacy VLANs | Are in Running-Config
1, 1002 – 1005 are auto created and cannot be deleted | Supports fewer VLAN features
Stored in the vlan.dat file in flash | Requires VTP configurations
VTP can synchronize between switches | 
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.1 – VLAN Ranges on Catalyst Switches

## Slide 14: VLAN Configuration VLAN Creation Commands
  VLAN details are stored in the vlan.dat file. You create VLANs in the global configuration mode.
Task | IOS Command
Enter global configuration mode. | Switch# configure terminal
Create a VLAN with a valid ID number. | Switch(config)# vlan vlan-id
Specify a unique name to identify the VLAN. | Switch(config-vlan)# name vlan-name
Return to the privileged EXEC mode. | Switch(config-vlan)# end
Enter global configuration mode. | Switch# configure terminal
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.2 – VLAN Creation Commands

## Slide 15: VLAN Configuration VLAN Creation Example
If the Student PC is going to be in VLAN 20, we will create the VLAN first and then name it.
If you do not name it, the Cisco IOS will give it a default name of vlan and the four digit number of the VLAN. E.g. vlan0020 for VLAN 20.
Prompt | Command
S1# | Configure terminal
S1(config)# | vlan 20
S1(config-vlan)# | name student
S1(config-vlan)# | end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.3 – VLAN Creation Example

## Slide 16: VLAN Configuration VLAN Port Assignment Commands
Once the VLAN is created, we can then assign it to the correct interfaces.
Task | Command
Enter global configuration mode. | Switch# configure terminal
Enter interface configuration mode. | Switch(config)# interface interface-id
Set the port to access mode. | Switch(config-if)# switchport mode access
Assign the port to a VLAN. | Switch(config-if)# switchport access vlan vlan-id
Return to the privileged EXEC mode. | Switch(config-if)# end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.4 – VLAN Port Assignment Commands

## Slide 17: VLAN Configuration VLAN Port Assignment Example
We can assign the VLAN to the port interface.
Once the device is assigned the VLAN, then the end device will need the IP address information for that VLAN
Here, Student PC receives 172.17.20.22
Prompt | Command
S1# | Configure terminal
S1(config)# | Interface fa0/18
S1(config-if)# | Switchport mode access
S1(config-if)# | Switchport access vlan 20
S1(config-if)# | end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.5 – VLAN Port Assignment Example

## Slide 18: VLAN Configuration Verify VLAN Information
Use the show vlan command. The complete syntax is:
show vlan [brief | id vlan-id | name vlan-name | summary]
Task | Command Option
Display VLAN name, status, and its ports one VLAN per line. | brief
Display information about the identified VLAN ID number. | id vlan-id
Display information about the identified VLAN name. The vlan-name is an ASCII string from 1 to 32 characters. | name vlan-name
Display VLAN summary information. | summary
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.8 – Verify VLAN Information

## Slide 19: VLAN Configuration Change VLAN Port Membership
There are a number of ways to change VLAN membership:
re-enter switchport access vlan vlan-id command
use the no switchport access vlan to place interface back in VLAN 1
Use the show vlan brief or the show interface fa0/18 switchport commands to verify the correct VLAN association.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.9 – Change VLAN Port Membership

## Slide 20: VLAN Configuration Delete VLANs
Delete VLANs with the no vlan vlan-id command.
Caution: Before deleting a VLAN, reassign all member ports to a different VLAN.
Delete all VLANs with the delete flash:vlan.dat or delete vlan.dat commands.
Reload the switch when deleting all VLANs.
Note: To restore to factory default – unplug all data cables, erase the startup-configuration and delete the vlan.dat file, then reload the device.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.10 – Delete VLANs
3.3.11 – Syntax Checker – VLAN Configuration

## Slide 21: 3.4 VLAN Trunks
Notes: 3 – VLANs
3.4 – VLAN Trunks

## Slide 22: VLAN Trunks Trunk Configuration Commands
Configure and verify VLAN trunks. Trunks are layer 2 and carry traffic for all VLANs.
Task | IOS Command
Enter global configuration mode. | Switch# configure terminal
Enter interface configuration mode. | Switch(config)# interface interface-id
Set the port to permanent trunking mode. | Switch(config-if)# switchport mode trunk
Sets the native VLAN to something other than VLAN 1. | Switch(config-if)# switchport trunk native vlan vlan-id
Specify the list of VLANs to be allowed on the trunk link. | Switch(config-if)# switchport trunk allowed vlan vlan-list
Return to the privileged EXEC mode. | Switch(config-if)# end
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.1 – Trunk Configuration Commands

## Slide 23: VLAN Trunks Trunk Configuration Example
The subnets associated with each VLAN are:
  VLAN 10 - Faculty/Staff - 172.17.10.0/24
  VLAN 20 - Students - 172.17.20.0/24
  VLAN 30 - Guests - 172.17.30.0/24
  VLAN 99 - Native - 172.17.99.0/24
F0/1 port on S1 is configured as a trunk port.
Note: This assumes a 2960 switch using 802.1q tagging. Layer 3 switches require the encapsulation to be configured before the trunk mode.
Prompt | Command
S1(config)# | Interface fa0/1
S1(config-if)# | Switchport mode trunk
S1(config-if)# | Switchport trunk native vlan 99
S1(config-if)# | Switchport trunk allowed vlan 10,20,30,99
S1(config-if)# | end
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.2 – Trunk Configuration Example

## Slide 24: VLAN Trunks Verify Trunk Configuration
Set the trunk mode and native vlan.
Notice sh int fa0/1 switchport command:
Is set to trunk administratively
Is set as trunk operationally (functioning)
Encapsulation is dot1q
Native VLAN set to VLAN 99
All VLANs created on the switch will pass traffic on this trunk
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.3 – Verify Trunk Configuration

## Slide 25: VLAN Trunks Reset the Trunk to the Default State
Reset the default trunk settings with the no command.
  All VLANs allowed to pass traffic
  Native VLAN = VLAN 1
Verify the default settings with a sh int fa0/1 switchport command.
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.4 – Reset the Trunk to the Default State

## Slide 26: VLAN Trunks Reset the Trunk to the Default State (Cont.)
Reset the trunk to an access mode with the switchport mode access command:
  Is set to an access interface administratively
  Is set as an access interface operationally (functioning)
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.4 – Reset the Trunk to the Default State (Cont.)